## Slide 1
Kalman Filter
and
Extended Kalman Filter(EKF)
By
Weitao Xiong
Advisor:
Prof. Hongfei Xue

## Slide 2
Kalman Filter
Seminal paper by R.E.Kalman, 1960
Set of mathematical equations
Optimal estimator
minimum mean square error
Versatile
  Estimation
  Filtering
  Prediction
  Fusion

## Slide 3
Kalman Filter: Start with an simple example
We start a car in position X_(k-1) and drive it at a constant speed. We want to track where our car is at time k. It seems very simple because we know the formula is
Convert them to a matrix
However, it is not perfect. In the real world, there exists many noise and uncertainty. So we can’t just use an input that you get from the sensor to put it in a formula to get an actual result.

## Slide 4
We can just assume that the velocity and position we get from the sensor are Gaussian distributed. Because when only the mean and variance are known, the Gaussian distribution is the most reasonable choice for modeling uncertainty because it makes the least assumptions about unknown factors.
We know that these two variables are correlated, and might their relationship look like this.
But How can we figure out this relationship?
Internal Noise and uncertainty

## Slide 5
We can capture it by using the covariance. It represents your uncertainty about the state of the system
Covariance matrices P_k are often labeled “Σ”, so we can write
Next page we will talk about the four element in the matrix
: Covariance matrices
: Position at k time

## Slide 6
The first diagonal element represents the uncertainty of the position
The second diagonal element represents the uncertainty of the velocity
The rest of the two represents the correlation between noise in measurements to the speed and to the position of the car

## Slide 7
We can represent this prediction step with a matrix, F_k

## Slide 8
Then we can update our covariance matrix
We know the formula below
However, it is not done yet, because there also exists External influence and External uncertainty

## Slide 9
For example, if the state models the motion of a train, the train operator might push on the throttle, causing the train to accelerate.
Similarly, in our robot example, the navigation software might issue a command to turn the wheels or stop. If we know this additional information about what’s going on in the world, we could stuff it into a vector called u_k, do something with it, and add it to our prediction as a correction.
External Influence is the thing in the outside world that could be affecting or controlling the system.
External Influence

## Slide 10
If we know the expected acceleration “a” due to the throttle setting or control commands. Then we can update our formula
In matrix form:
: is called the control matrix

## Slide 11
For example, if we’re tracking a quadcopter, it could be buffeted around by wind. If we’re tracking a wheeled robot, the wheels could slip, or bumps on the ground could slow it down.
External Uncertainty
External Uncertainty is something we can’t track outside.
This produces a new Gaussian blob, with a different covariance (but the same mean)

## Slide 12
In other words, the new best estimate is a prediction made from the previous best estimate, plus a correction for known external influences.
And the new uncertainty is predicted from the old uncertainty, with some additional uncertainty from the environment.

## Slide 13
Each sensor tells us something indirect about the state— in other words, the sensors operate on a state and produce a set of readings.
Refining the estimate with measurements

## Slide 14
Notice that the units and scale of the reading might not be the same as the units and scale of the state we’re keeping track of.
So we’ll model the sensors with a matrix, H_k.

## Slide 15
From each reading we observe, we might guess that our system was in a particular state. But because there is uncertainty, some states are more likely than others to have produced the reading we saw.
We’ll call the covariance of this uncertainty (i.e. of the sensor noise) R_k.
The distribution has a mean equal to the reading we observed, which we’ll call z_k.

## Slide 16
We must try to reconcile our guess about the readings we’d see based on the predicted state (pink) with a different guess based on our sensor readings (green) that we actually observed.
If we have two probabilities and we want to know the chance that both are true, we just multiply them together. So, we take the two Gaussian blobs and multiply them.

## Slide 17
Combining Gaussians
For more detail about how to deduct the formula, you can see the paper Kalman Filter: Multiplying Normal Distributions
https://www.Norbert-freier.de/dateien/kalman_filter_multiplying_normal_distributions_norbert_freier_2013.pdf
z1
z2
After we multiply two of the distributions, We can get a new one

## Slide 18
K is a matrix called the Kalman gain
Convert in matrix version:
We can simplify as below：

## Slide 19
Predicted Measurement:
Observed Measurement:
Then we can convert these
as below
Estimated
Stated

## Slide 20
We can knock an H_k off the front of every term in
And an H_k.T off the end of all terms in the equation for P_k’.

## Slide 21
is our new best estimate, and we can go on and feed it (along with ) back into another round of prediction or update as many times as we like.
If close to 0, means our prediction is well!

## Slide 22
Summary

## Slide 23
Extended Kalman Filter
(EKF)

## Slide 24
Extended Kalman Filter (EKF)
Just focus on First-order terms
Hint: Linearization treatment of nonlinear systems
Use Taylor Expansion

## Slide 25
Linearized motion model
Linearized measurement model
Jocabian
Matrices

## Slide 26
Jacobian Matrices
For example:

## Slide 27
The rest part is the same as the Kalman Filter
We could see more detail in the Project1